Tode-SIOST-CB.241P
Hardware Development
Side-IO Screw Terminals - Commercial Box

by TGit-Tech [ http://www.TGit-Tech.com ] Last Updated: 2024-01-25
Compatible with [S]ide-IO Tode-RCs - Models: SD23CF
Fitted for Joinfworld 6x6x4 Outdoor Box Enclosure with Clear Lid.

This guide covers everything needed to build the Screw Terminals (Right of Tode).
Screw Terminals can be used inside or outside an enclosure.

# Table of Contents

TOTAL Screw-Terminals with Outdoor Enclosure:	$32.04
# Screw Terminal Block
## Bill of Materials (BOM) $5.84
### Parts $1.66
Bottom PCB / Design Software: Kicad / Folder: \Tode-IO\Side-IO 3D-Printed Box\kicad\SIOST-BOTTOM\SIOST / Manufacturer: jlcpcb.com / Batch Price: $33.96 per 100 / Pricing: $0.34/ea
Top PCB / Design Software: Kicad / Folder: \Tode-IO-Options\Side-IO 3D-Printed Box\kicad\SIOST-TOP\SIOST / Manufacturer: jlcpcb.com / Batch Price: $10.11 per 50 / Pricing: $0.20/ea
(2) KY-019 5V 1-Channel Relay Module Board / $0.56/ea = $1.12

### Supplies $3.18
(1) 1x10P 90° Male Pin Header / Dupont 2.54mm-Pitch / For Side-IO Plug / @$0.10/ea = $0.10		(1/2-Sheet) Adhesive Shipping Label / @0.04/sheet = $0.02
		2-Inch Clear Packing Tape / Weatherproof Label
(9) CUI 1x2P Screw Terminals / 5.08mm Pitch / @$0.30/ea = $2.70		(1) #2 x 1/4”Phillips-Pan Screw / Standoff-Label / $0.04/ea = $0.04
(2) #4 x 3/4” Phillips-Pan Screws / Standoff-HighRelay / $0.08/ea = $0.16		(4) #2 x 1/4” Phillips-Flat Screw / Relays / $0.04/ea = $0.16

### 3D-Prints $1.00

SIOST-1W.stl / Folder: ./Tode-IO-Options/Side-IO Commercial Box/3DPrints/stl / Layer Height: 0.2mm / Infill Density: 100% / Supports: OFF / Plastic: 24-grams @ $0.02/g = $0.48 / Printer-use: @ $0.0015/g = $0.036 / Power: 3h 02m @ $0.01/hr = $0.03 / TOTAL COST: $0.546
SIOST-Standoff-HighRelay.stl / Folder: ./Tode-IO-Options/Side-IO Commercial Box/3DPrints/stl / Layer Height: 0.2mm / Infill Density: 100% / Supports: OFF / Plastic: 19-grams @ $0.02/g = $0.38 / Printer-use: @ $0.0015/g = $0.0285 / Power: 2h 52m @ $0.01/hr = $0.03 / TOTAL COST: $0.4385
SIOST-Standoff-Label.stl / Folder: ./Tode-IO-Options/Side-IO Commercial Box/3DPrints/stl / Layer Height: 0.2mm / Infill Density: 100% / Supports: OFF / Plastic: 1-grams @ $0.02/g = $0.02 / Printer-use: @ $0.0015/g = $0.0015 / Power: 0h 09m @ $0.01/hr = $0.00 / TOTAL COST: $0.0215

## Diagram
BOTTOM-PCB Layout
BOTTOM-PCB SCHEMATIC	TOP-PCB LAYOUT

## PCB Assembly

Bottom PCB / Solder on (4) CUI screw terminals / Solder on (10) Right Angle Pin Header / Solder on Black Jump wire
Top PCB / Install 1x6P Header; push pins down flat with top-side and solder from back-side. / Solder on (5) CUI Screw Terminals.
LED / Attach 1x6P Socket to Pins
Put Standoff in place / Put Top PCB on Standoff with 1x6P Socket aligned with Bottom-PCB holes.
Solder the 1x6P Socket to Bottom-PCB.

## Casing Assembly
Terminal Block / Plug the Top PCB over the Standoff. / Using (2) #4 x 3/4” Phillips-pan screw fasten Top PCB to SIOST-1W 3DPrint.
Relays / Place (2) Relay Modules onto Standoff and fasten them using (4) #2 x 1/4” Phillips-Flat Screws.
Labels / Print Label / Stick Label to Labels 3DPrint using 2-Inch Packing Tape wrapped all the way around. / Use Scissors to cut-of excess tape. / Screw Label above the Relays

# Outdoor Enclosure
## Bill of Materials (BOM) $26.20
### Parts $26.20

Commercial Box / Manufacturer: Joinfworld / Retail Dimensions: 6x6x4 / Cover: Clear / Outside Dimensions: 5.9 x 5.9 x 3.9 / Inside Dimensions: / Link https://www.amazon.com/Joinfworld-Outdoor-Electrical-Box/dp/B0CHHJ49QN?th=1 / $19.99/ea = $19.99

SMA Extension Cable / Female SMA Right Angle / Male SMA Straight / 5-Meters Long / $6.21/ea = $6.21